## Design Example: CMOS Differential-pair with Constant-gm Biasing, FREEPDK45

Figure 1: Diff-pair with Constant-gm Biasing
Specifications:
VDD = 1.8V, GBW = 120e6 Hz, CL = 10 pF, with freePDK45 process node technology

-V_P - V_SG - V_SDsat + V_DDA = 0 "and" -V_P - V_SG + V_SDsat + V_GS = 0
V_GS - V_SG + V_SDsat "<" V_"IN,CM" "<" V_DDA - V_SG - V_SDsat
→ Start with M1 (and M2)
- From CL and GBW: g_"m,M1" = 2%pi f_u ( 1 + 0.2 )C_L = 2 %pi cdot 120e6 cdot 1.2 cdot 10e-12 = 9.04e-3 S , where the factor 0.2 is to capture some parasitic capacitance
- Since we don’t have a specific power consumption spec here, we pick g_m/I_D = 15 (MI) for M1 since it is a gain stage
I_D = { g_"m,M1" } over { g_m/I_D } = 9e-3 over 15 = 603.18 uA
- From I_D / W vs g_m/I_D plot ( LUT ) of PMOS, we determine (there could be some other different candidates)

Figure 2: I_D / W vs g_m/I_D plot ( LUT ) of PMOS
for L = 125 nm, g_m / I_D = 15 we have I_D over W = 7.96
W_M1 = I_D over J_D = 603e-6 over 7.96 = 75.75 um
(If you have any DC gain requirement, you can increase LM1 by looking at g_m/g_ds vs. g_m/I_D plot , which will give you a new WM1.)

Figure 3: g_m/I_D vs V_SG
"from" g_m / I_D = 15 vs V_GS for L = 125 nm toward V_GS = -0.572V

→ Second, we design M3 (and M4)
- Since we don’t have a specific power consumption spec here, we pick g_m /I_D = 10 for M3 since it is an active load (source), so it should be smaller
- Since we know I_"D,M3" = I_"D,M1" = 603 uA already from the calculation of M1, from I_D / W vs g_m / I_D plot ( LUT ) of NMOS , we determine (there could be some other candidates)

Figure 4: I_D / W vs g_m / I_D plot ( LUT ) of NMOS
for L = 600nm, g_m / I_D = 10, we have I_D / W = 12.54
W_M3 = I_D over J_D = 603e-6 over 12.54 = 48.08 um
The active load and current source should have larger output impedance, therefore L is intentionally picked larger value.
→ Third, we design current mirror M5 (and M6)
- For simplicity here, we assume M5 and M6 have the same dimension (can be scaled down later for reducing power consumption(
- Since we don’t have a specific power consumption here, we pick g_m / I_D = 4 for M5 since it is active load (source), a device whose gm does not contribute to gain and should have a good matching we pick the transonductance effficeiency in SI (The mismatch is independent of transistor width in strong inversion. The only way to improve the matching is to employ a longer channel.)
The g_m / I_D is even smaller than M3’s since here, I_"D,M5" = 2I_"D,M3" , smaller g_m / I_D can give larger L values, which is desirable for current mirror design
- Since we know I_"D,M5" = 2I_"D,M1" = 1.2e-3 A , already from the calculation of M1, from I_D / W vs g_m / I_D plot ( LUT ) of PMOS Figure 2 we determine (there could be some other different candidates)
for L = 1.2e-6, g_m / I_D = 4 we have I_D/ W = 12.93
W_M5,6 = I_D over J_D = 1.2e-3 over 12.93 = 92.8um
Now, we can start designing the constant-gm biasing block
Analysis:
## →NMOS implementation of constant-gm biasing circuit

Figure 5: NMOS implementation
## → PMOS implementation of constant-gm biasing

Figure 6: PMOS implentation
## Analysis:

Figure 7: Gm of NMOS with RB in source
→ an analysis of the M15 and RB subcircuit from Figure 5, shown in Figure 7 will show that Gm of this circuit is equal to 1/RB
G_m = {i_out} over {v_"in"}
i_out - gmv_gs = 0 toward i_out = gmv_gs
-R_"B"i_out - v_gs + v_"in" = 0 toward v_"in" = R_"B"i_out + v_gs
toward G_m = gmv_gs over { R_"B"i_out + v_gs } = gmv_gs over { R_"B"gmv_gs + v_gs } approx 1 / R_B
→ to keep gm constant in Figure 5 we need gm_13 = 1 / R_B , this way if we can select gm through g_m/I_D , we can set RB to give us a specific current for biasing our amplifier
Now we will analyse Figure 5, to get the needed aspect ratios to have gm_13 = 1 / R_B :
-R_"B"I_D15 - V_GS15 + V_GS13 = 0
V_GS = V_T + sqrt{ {2 I_D} over { k_n^{'} W over L } }, strong inversion, square-law design
if I_D15 = I_D13
R_"B"I_D = sqrt{ {2 I_D} over { k_n^{'} W_{13} over L_{13} } } - sqrt{ {2 I_D} over { k_n^{'} W_{15} over L_{15} } }
we need g_m = sqrt { 2 %mu C_ox W over L I_D } = 1 over R_B "in" strong inversion, with square-law design
R_"B"I_D = evaluate {sqrt{2 I_D} left ( 1 over sqrt{{ k_n^{'} W_{13} over L_{13} } } - 1 over sqrt{{ k_n^{'} W_{15} over L_{15} } } right )} to{2}
toward R_B^{2} I_D^{2} = 2 I_D evaluate left ( 1 over {k_n^{'}W_{13} over L_{13}} + 1 over {k_n^{'}W_{15} over L_{15}} - 2 1 over {k_n^{'}sqrt{W_{13} over L_{13} W_{15} over L_{15}}}right ) cdot k_n^{'}
toward k_n^{'}R_B^{2} I_D = 2 left ( 1 over {W_{13} over L_{13}} + 1 over {W_{15} over L_{15}} - 2 1 over {sqrt{W_{13} over L_{13} W_{15} over L_{15}}}right )
here the "right" hand element, i.e., 2 left ( 1 over {W_{13} over L_{13}} + 1 over {W_{15} over L_{15}} - 2 1 over {sqrt{W_{13} over L_{13} W_{15} over L_{15}}}right ), must be equal "to" 1 over { 2 W_{13} over L_{13} }
so that g_m = sqrt { 2 %mu C_ox W over L I_D } = 1 over R_B
toward 2 left ( 1 over {W_{13} over L_{13}} + 1 over {W_{15} over L_{15}} - 2 1 over {sqrt{W_{13} over L_{13} W_{15} over L_{15}}}right ) = 1 over { 2 W_{13} over L_{13} }
"and" after furher algebraic analysis we find 4 W_{13} over L_{13} = W_{15} over L_{15}
toward k_n^{'}R_B^{2} I_D = 2 left ( 1 over {W_{13} over L_{13}} + 1 over {4W_{13} over L_{13}} - 2 1 over {sqrt{W_{13} over L_{13} 4W_{13} over L_{13}}}right )
toward k_n^{'}R_B^{2} I_D = 2 left ( {4 + 1} over {4W_{13} over L_{13}} - 2 1 over {2W_{13} over L_{13} }right ) = {10} over {4W_{13} over L_{13}} - 2 over {W_{13} over L_{13}} = { 10 -8 } over {4W_{13} over L_{13}} = 1 over { 2W_{13} over L_{13} }
toward evaluate {2k_n^{'}W_{13} over L_{13} I_D = 1 over { R_B^{2} }} to{sqrt2} toward sqrt{ 2k_n^{'}W_{13} over L_{13} I_D } = 1 over R_B
We arrive at, g_"m,M7" = 1/ { R_BIAS } if W_M8 = 4W_M7 , where this were calculated as with long channels and strong-inversion equations.
If we let M1 and M7 have the same size, and if we can somehow let M1 and M7 have the same gm, then their ID will also be the same.
Design RBIAS:
Letting g_m1 = g_m7: g_m1 = g_m / I_D cdot I_"d,M1" = 9e-3 S
R_BIAS = 1 over { g_"m7" } = 111 %OMEGA
→ Design M7 (and M8)
- Simply copying M1 to M7: W_M1 = W_M7 = 75.75um; L_M1 = L_M7 = 125 nm
- Rather than making W_M8 = 4W_M7 , we can let W_M8 = W_M7 and use multiplier M_M8 = 4M_M7 (you can aproximate its value by SPICE simulations, as the equations used for this example are not accurate)
→ Design M9 (M10 and M11)
- Simply copying M3 to M9, M10
- For M11 we simply double the width of M9
- If necessary you can increase L of M9, M10 and M11 to increase the output resistance of current mirror, ensuring you are always operating them in saturation region.

Figure 8: Diff-Amp with Aspect Ratios for GBW ~120 MHz with freePDK45

Figure 9: GBW representation ~ 120 MHz
## Appendix
Note: If you are designing by Av0 as a specification parameter, then L and g_m/I_D will play a significant role as seen in Figure 10, where
A_v0 = { g_m1 over { g_ds2 + g_ds4 } }
toward A_v0 = { g_m1/I_D } over { {g_ds2 over I_D} + {g_ds4 over I_D}}

Figure 10: A_v0 vs ( g_m/I_D )
Av0 will also tradeoff with ft Figure 11, and implicitly fu of the circuit:

Figure 11: A_v0 vs f_t